## Slide 1: Cloud RTR: Cloud Infrastructure for Apps with Hardware
Thesis Defense – April 16th 2015
Ali Yasser Ismail

## Slide 2: Goal

## Slide 3
Apps with Hardware (Mōbware)
Smart Phone
The App Store
Give mobile phones re-programmable hardware (FPGA)
Allow applications to utilize hardware
Give developers a way to create and deploy their own hardware
App + HW
App + HW

## Slide 4: Benefits

## Slide 5
What do we gain?
New Hardware Functionality
  Software Defined Radio
  Digital Signal Processing Hardware (FFT and FIR)
  Cryptography Processing Hardware(AES and RSA)
Better Performance
  Microsoft accelerates datacenters with FPGA (Project Catapult)
  (Intel in talks to acquire Altera)
Power Savings

## Slide 6
Case Study 1
Possa et al. [2]
  Implemented a 15th order FIR filter
  Compared FIR software implementation to hardware implementation
  Used Nios II 32-bit RISC embedded processor and Altera Cyclone III FPGA

## Slide 7
Case Study 2
Che et al. [4]
  Studied performance of GPU vs FPGA
  Implemented 3 Applications
    Gaussian Elimination (Linear Algebra)
    DES (64-bit block – FPGA took 83 cycles and GPU took 5.80 x 105 cycles)
    Needleman-Wunsch (DNA Sequencing)
  Hardware Used
    Intel Xeon Processor (3.2 GHz, 4 Threads)
    NVIDIA GeForce 8800 GTX (128 stream processors at 575 MHz)
    Xilinx Virtex-II Pro (100 MHz)

## Slide 8
Case Study 2 Cont.

## Slide 9
FPGA’s in cell phones!
Industry moving towards SoCs
  Off-the-shelf systems with FPGA’s and ARM Cortex A9 coupled together on the same chip
High Level Synthesis (HLS) tools gaining momentum
  Built-in Libraries
  Simple IP generation process
  Test Environment
Xilinx supports run-time reconfiguration
  Partial Reconfiguration Technology [5]
Notes: Mention that ARM cortex A9 is both present on this SoC and in the Iphone

## Slide 10: Challenges

## Slide 11: Run-time Reconfiguration Approaches

## Slide 12
Option 1: Reconfigure the Entire FPGA Design
Re-define and compile an FPGA design
Deploy
Advantage
  Simple
Disadvantages
  Disrupt other running hardware
  Must compile and then deploy (Expensive)
  Slow

## Slide 13
Option 2: Xilinx Partial Reconfiguration
Hardware Developer wants to support design variants
  Not enough space
  Flexibility
Hardware Developer Design
  FIR Filter
  Swap 15 tap filter with 20 tap filter
Xilinx Design Flow
  Define partitions in the FPGA
  Define Reconfigurable Modules (Variants)
  Place RMs into each partition, place & route, generate full and partial bitstreams

## Slide 14
Option 2: Xilinx Partial Reconfiguration
Advantage
  Supported in Xilinx mainstream tools (Vivado)
  Floor planning is done by hand, thus, area is used optimally
Disadvantages
  Not general, everything known at compile time
  Everything dictated by the developer, thus, does not support multiple party involvement

## Slide 15
But this is what we want!
Support for multiple parties
  Phone Manufacturers (Static Design)
  Developers (Reconfigurable Modules)
  User (End-System)
Phone manufacture and developer do not have control of end system
Need a general deployment model!
Phone Manufacturers
Developers
User

## Slide 16
Option 3: General RTR (Academic)
Two main approaches to obtain general RTR
  Run-time place & route
  Pre-defined slots
Many variations of the two approaches in decades of work

## Slide 17: Run-time Place & Route

## Slide 18
Run-time Place & Routing
Developer provides “source” design
End system handles place route at runtime to integrate into the design (more general)
General Limitations
  Tied to specific architectures
  Not adopted in mainstream tools
  Forced to reverse engineer bitstreams
  Inefficient (Slow, doesn’t always work, poor performance)

## Slide 19
Run-Time Routing Related Work
JBits – API into Xilinx bitstream[11]
  API to access Xilinx FPGA bitstream
  Access to LUTs, routing, Flip-Flops
JRoute [12]
  API that routes Xilinx FPGA devices
  Routing at run-time
Slotless Module-Based Reconfiguration [13]
  Compile-time vs Run-time
  Allocate large sandbox (Place Modules Optimally)
  BitShop
Notes: At compile time, they compile individual module that have been wrapped (handle feed-through signals and connections to adjacent modules) and fitted with Latol.
At run-time, place modules in sand-box, route channels, and complete module connections

## Slide 20: Slot-based Solutions

## Slide 21
Slot-based Run-time Reconfiguration
Pre-placed slots in the FPGA
Download configuration bits to the slots
General Limitations
  Forced to reverse engineer bitstreams
  Force heavy constraints on routing

## Slide 22
Slot-based Related Work
Horta et al. [14] 2002
  Dynamic Hardware Plugins (Slots)
  PARBIT
    Original bitfile
    Target bitfile
    Configuration Parameters
  Routing constraints happen during static design bitstream generation
Notes: First need a target bitfile that contains DHPs
From original bitfile, extract module wanted to relocate.
Module is extracted and placed into target bitfile

## Slide 23: Our New Approach

## Slide 24
Our Approach
Use Xilinx mainstream tools to create a general RTR solution
How?
  Leverage deployment model of apps

## Slide 25
Cloud RTR Approach
Consumer
Manufacturer
The Cloud Compiler
Google Play Store
App3 + partial bitstream3
App2 + partial bitstream2
App1 + partial bitstream1
App4 + partial bitstream4
Developer
Notes: Cloud deployment of partial bitstreams
  Compilation occurs when uploaded by developer
  User not forced to wait, compilation has already occurred
Use brute force compilation method
  Can use Xilinx tools as is (handles PR)
  Bitstream manipulation and quick routing is unnecessary

## Slide 26: Our Contributions

## Slide 27
Our Contributions
Worked out nuances of Xilinx partial reconfiguration [5]
  Developed tools to automate and simplify this process
Built cloud-based system and did an evaluation of the brute-force method

## Slide 28: Partial Reconfiguration

## Slide 29
Background Terms
Synthesis
  HDL into a netlist (connecting gates or flip-flops)
Place & Route (Implementation)
  Process to place and map netlist to FPGA physical resources
Partial Reconfiguration (PR)
Reconfigurable Module (RM)
Processing System (PS)
  ARM Cortex A9
Programmable Logic (PL)
  FPGA (Fabric)
Out-of-context (OOC) Synthesis
  Separate netlist for module
  No optimizations

## Slide 30
Define Static Design
Hardware needed by RM
  DMA
  Reset Hardware
PS
GPU
AXI
HDMI
Interconnect
AXI
Reset
DMA
AXI
AXI
RM
AXI
I/O
AXI

## Slide 31
PR Clock Boundary
Placing partitions on clock was not enough
CPU
Reset
RM
FPGA
P
P
P
P
P
AXI

## Slide 32
Static Design Synthesis
Before any PR can be done we need to instantiate black boxes in HDL static design
Need to make sure interfaces match
Static Design (HDL)
Static Design (Gates)
1
2
3

## Slide 33
Static Design Synthesis
HDL generated by Vivado from block design
Script to instantiate black boxes

## Slide 34
Base PR Tool Flow
Configure black boxes to be reconfigurable
Load a design into each partition*
Floorplan each block on a clock boundary
Implement design (Place & Route)
Carve out partitions
Save base checkpoint
FPGA
P
P
P
P
P
P
Static Routed Checkpoint
Base Implementation Checkpoint
Static Design (Gates)
1
2
3
R
D
R
R
D
D
* Each design must be synthesized OOC so they can be loaded in the partition

## Slide 35
Dynamic PR Tool Flow
Lock Design
Load RM into each partition
Implement design (Place & Route)
Verify
Generate Bitstreams/Binaries
Static Routed Checkpoint
P
P
P
Base Implementation Checkpoint
Dynamic Implementation Checkpoint
Verify
PASS
Full Bitstream
Partial Bitstream1
Partial Bitstream2
Partial Bitstream3
* Each design must be synthesized OOC so they can be loaded in the partition

## Slide 36: Evaluation

## Slide 37
Experiments
Experiment 1: Slot Placement
  Place max # of FFT’s
  1024 samples/frame
  Single channel
  16-bit data width
Experiment 2: Base PR execution times
  2 – 8 FFT slots
Experiment 3: Dynamic PR execution times
  2 – 8 FFT slots
How many slots will be available to developer/user?
Is the brute force method practical?

## Slide 38: Experiment 1

## Slide 39
How many slots?
Slot Placement
  Place max # of FFT’s
  1024 samples/frame
  Single channel
  16-bit data width
Resources Available
  Slices
  BRAM
  DSPs
Result
  Placed 8 FFT’s

## Slide 40
FPGA Layout

## Slide 41
FFT Slot Layout

## Slide 42
Slot Design Layout Considerations
What did we learn?
  Best to allocate all three resources to slots
  DSPs and/or Slices will likely be bottleneck
  Potentially reduce number of slots and allocate more space
  Hardware support will grow with RMs (Less slots means more space can be used)
Hardware | Most Used Resource | % Utilization
FFT IP | LUTs | 6.12
Reset IP | LUTs | 0.07
DMA IP | LUTs | 2.21

## Slide 43: Experiment 2

## Slide 44
Base PR Execution Time
Intel Xenon 2.1 GHz (6 cores with 48 GB RAM)
2 – 8 Slots
FFT
  1024 samples/frame
  Single channel
  16-bit data width
Note: This process is done once for each phone variant (or when manufacturer updates static design)

## Slide 45
Base PR Execution Time
Chart: # of Slots
| 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 6.0167 | 9.1833 | 12.25 | 16.5667 | 22.0167 | 27.7 | 36.1667

## Slide 46
Slot Design Layout Considerations
What did we learn?
  More area means more compilation time
Placement of slots affect compilation time
  Solution: Use a bigger FPGA or less FPGA area

## Slide 47: Experiment 3

## Slide 48
Dynamic PR Execution Time
Intel Xenon 2.1 GHz (6 cores with 48 GB RAM)
2 – 8 Slots
FFT
  1024 samples/frame
  Single channel
  16-bit data width

## Slide 49
Dynamic PR Execution Time
Chart: # of Slots
| 2 | 3 | 4 | 5 | 6
 | 8.21 | 11.22 | 15.31 | 20.5 | 24.52

## Slide 50
Slot Design Layout Considerations
Placement of slots affect compilation time more prevalent in dynamic PR flow
Solution: Use a bigger FPGA or less FPGA area

## Slide 51: Cloud RTR Deployment Requirements

## Slide 52
Google Play Store Figures | 
# of Apps as of Dec 14 | 1.43 Million
Average Monthly App Growth | 6.10%
# of Apps for April 15 | 104,187
Google Play Store

## Slide 53
Compilation Times |  |  | 
# of Slots | Execution Time (M) | RM Synthesis Execution Time(M) | Total Execution Time (M)
2 | 8.21 | 3.71 | 11.92
3 | 11.22 | 3.71 | 14.93
4 | 15.31 | 3.71 | 19.02
5 | 20.50 | 3.71 | 24.21
6 | 24.52 | 3.71 | 28.23
Dynamic PR Compilation Latency

## Slide 54
Dynamic PR Compilation Throughput – 2 Slots
Max # of Apps Compiled per day | 
# of Slots | Apps
2 | 121
3 | 96
4 | 76
5 | 59
6 | 51
2 Slots Requirements | % of April Apps that use Hardware (# of Apps Uploaded per Day) |  | 
 | 0.1 (3.47) | 1 (34.72) | 10(347.28)
# of Phone Architectures | # of Machines Required to Compile Apps |  | 
1 | 0.03 | 0.29 | 2.87
10 | 0.29 | 2.87 | 28.75
100 | 2.87 | 28.75 | 287.48
1000 | 28.75 | 287.48 | 2874.78

## Slide 55
Dynamic PR Compilation Throughput – 6 Slots
Max # of Apps Compiled per day | 
# of Slots | Apps
2 | 121
3 | 96
4 | 76
5 | 59
6 | 51
6 Slots Requirements | % of April Apps that use Hardware (# of Apps Uploaded per Day) |  | 
 | 0.1 (3.47) | 1 (34.72) | 10(347.28)
# of Phone Architectures | # of Machines Required to Compile Apps |  | 
1 | 0.07 | 0.68 | 6.81
10 | 0.68 | 6.81 | 68.08
100 | 6.81 | 68.08 | 680.83
1000 | 68.08 | 680.83 | 6808.31

## Slide 56
Moving Forward
So far…
  Proved PR works (Built many simple use cases)
  Proved PS can communicate with PL
  Proved that brute force method is viable and not many machines are required
  Base and dynamic PR has been automated and works for simple use cases
  Mike has designed more interesting use cases (Memory Scanner and AES)
  Mike has Android running on the zedboard and can read memory and load bitstreams
Looking forward…
  Determine best communication between PS and PL
  Create application that uses hardware (Mike is very close)
  Study Mikes use cases resource utilization
  Plan to submit to paper to Micro-48 (International Symposium on Microarchitecture 2015)

## Slide 57
Acknowledgements
The Team
  Advisor: Eric Keller
  Michael Coughlin
Xilinx Inc.
  Philip James-Roxby
  Derrick Woods
  Xilinx Forums
NGN Group

## Slide 58
References
[1] D. A. Patterson and J. L. Hennessy, Computer organization and design,"
M. Kauman, Ed., 2009.
[2] P. Possa, D. Schaillie, and C. Valderrama, Fpga-based hardware acceleration: A
cpu/accelerator interface exploration," in IEEE International Conference on
Electronics, Circuits and Systems (ICECS), 2011.
[3] C. Cullinan, C. Wayant, T. Frattesi, and X. Huang, Computing performance
benchmarks among cpu, gpu, and fpga," MathWorks. 2013.
[4] S. Che, J. Li, J. W. Sheaer, K. Skadron, and J. Lach, \Accelerating
compute-intensive applications with gpus and fpgas," in Symposium on Application
Specic Processors (SASP), 2008.
[5] Xilinx partial reconguration. [Online]. Available:
http://www.xilinx.com/tools/partial-reconguration.htm

## Slide 59
References
[6] M. Majer, J. Teich, A. Ahmadinia, and C. Bobda, \The erlangen slot machine: A
dynamically recongurable fpga-based computer," in VLSI Signal Processing Systems,
2007.
[7] D.Koch, C. Beckho, and J. Teich, \Recobus-builder a novel tool and technique to
build statically and dynamically recongurable systems for fpgas," in Proc. Field
Programmable Logic and Applications (FPL), 2008.
[8] C. Conger, R. Hymel, M. Rewak, A. George, and H. Lam, \Fpga design framework for
dynamic partial reconguration," in Proceedings of Recongurable Architectures
Workshop (RAW), 2008.
[9] S. Che, J. Li, J. W. Sheaer, K. Skadron, and J. Lach, \Accelerating
compute-intensive applications with gpus and fpgas," in Symposium on Application
Specic Processors (SASP), 2008.
[10] Xilinx partial reconguration. [Online]. Available:
http://www.xilinx.com/tools/partial-reconguration.htm

## Slide 60
References
[11] S. Guccione, D. Levi, and P. Sundararajan, “JBits: Javabased interface for reconfigurable computing”,
Proc. Conf. on Military and Aerospace Application of Programmable Devices and Technology, 1999.
[12] E. Keller, “JRoute: A run-time routing API for FPGA hardware.” in IPDPS Workshops, ser. Lecture
Notes in Computer Science, J. D. P. Rolim, Ed., vol. 1800. Springer, 2000, pp. 874–881
[13] C. Patterson, P. Athanan, M. Shelburne, J. Bowen, J. Suris, T. Dunham, and J. Rice,
Slotless module-based reconguration of embedded fpgas." in ACM Trans. Embedd.
Comput. Syst, October 2006.[8] C. Conger, R. Hymel, M. Rewak, A. George, and H. Lam, Fpga design
framework for dynamic partial reconguration," in Proceedings of Recongurable Architectures
Workshop (RAW), 2008.
[14] E. L. Horta, J. W. Lockwood, D. E. Taylor, D. Parlour, "Applications of reconfigurable computing:
Dynamic hardware plugins in an FPGA with partial run-time reconfiguration", Proceedings of the
39th conference on Design automation, New Orleans, June 2002, pp. 343 – 348

## Slide 61: Data Supplemental Slides

## Slide 62
Slot Resource Utilizations

## Slide 63
Base PR Execution Time
Note: Does not include bitstream generation or any verification

## Slide 64
Slot-based Related Work
Majer et al. [6] 2007
  Erlangen Slot Machine
  Automated tool flow called SlotComposer
  External Peripherals (Feed-Through Issue)
  Reconfiguration Manager

## Slide 65
Related Work Cnt.
Koch et al. [7] 2008
  Developed Recobus-Builder – A tool that supports building reconfigurable systems on FPGAs
  Simplifies the partial reconfiguration process
    Allowed for testing
    Optimal Floor planning
    Automated Partial Reconfiguration
  Limitations they solved
    Difficulty of PR tool flow
  Lacking
    Ignored multipurpose systems (Everything known at compile time)

## Slide 66
Better Performance and Less
Power?
Hit Power Wall 2000’s [1]
  Needed to find alternatives to increase performance and reduce power
  Solutions: Multiprocessors, GPU’s, FPGA’s

## Slide 67
Case Study 2
Cullin et al. [3]
  Implemented an FFT on CPU, GPU, and FPGA
  Compared each of their execution times
  Hardware Used
    Intel Xeon X5650 (1.6 GHz, 24 Threads) (69 ms)
    NVIDIA GeForce GTX 460 ( 675 MHz, 336 CUDA cores)
    NVIDIA GeForce 9800 GTX+ ( 738 MHz, 128 CUDA cores)
    Xilinx Virtex-5 (100 MHz)

## Slide 68
Understanding FPGA Resources
BRAM
Slices

## Slide 69
Design Considerations
Generate Tcl scripts (Ok, we wanted this)
Pre-defined floor plans (Fixed # of slots)
  Layout on clock boundries
Synthesize RMs separately
All interfaces have to match

## Slide 70
Related Work Cnt.
Conger et al. [8] 2008
  Developed a framework that addressed special purpose and multipurpose systems

## Slide 71
Slot-based Challenges
Allocate fixed size slots to contain RMs
Feed-through signals

## Slide 72
Phone Manufacturer
Cloud RTR Approach
Developer
Compiler
User
Notes: Cloud deployment of partial bitstreams
  Compilation occurs when uploaded by developer
  User not forced to wait, compilation has already occurred
Use brute force compilation method
  Can use Xilinx tools as is (handles PR)
  Bitstream manipulation and quick routing is unnecessary